## Slide 1: Graph-Based Behavior Modulation for Enhancing Multi-Agent Navigation
Javier Perera-Lago
Francisco-Jose Campos-Castro
JÉrÔme Guzzi
Rocio Gonzalez-Diaz

## Slide 2: PROBLEM TO SOLVE

## Slide 3: The goal: Autonomous Navigation
Consider a delimited area such as:
  A hospital
  A nursing home
The agents are autonomous wheelchairs.
The environment can have:
  Fixed obstacles (walls, tables, chairs…)
  Dynamic obstacles (pedestrians, other wheelchairs…)

## Slide 4: Navigation BEHAVIORS
To reach a target point, each agent follows a behavior.
A BEHAVIOR is a local navigation algorithm that:
  Analyses the position and velocity of nearby obstacles
  Computes a motion command trying to
    reach the target
    avoid collisions
There is NO COMMUNICATION between agents.
Some navigation behaviors are Human-Like, ORCA and Social Force

## Slide 5: NAVGROUND SIMULATOR
NAVGROUND is a Python library to test navigation behaviors in custom scenarios.
It is easily installable via pip.
All our code, experiments and animations are done with Navground.

## Slide 6: NEGATIVE EVENTS TO AVOID
COLLISIONS
  When an agent collides with other agents or with static obstacles
DEADLOCKS
  When an agent cannot move because it is blocked by other agents

## Slide 7: NEGATIVE EVENTS TO AVOID
The said behaviors cannot prevent collisions in a narrow region.
The said behaviors cannot prevent the formation of obstructive platoons.

## Slide 8: OUR PROPOSED SOLUTION

## Slide 9: BEHAVIOR MODULATION
A MODULATION is an algorithm complementing the behavior of an agent.
It can act before the behavior:
  Changing the agent’s perception of its environment
  Changing the agent’s motion parameters
It can act after the behavior:
  Changing the computed motion command
However, it does not change the behavior itself.
THE SAME MODULATION CAN BE APPLIED TO MANY DIFFERENT BEHAVIORS

## Slide 10: AGENT Representation
An agent is modelled as a tuple , with:
Center
Radius
Orientation
Safety margin

## Slide 11: NEEDED SPACE TO PASS BETWEEN OBSTACLES
Consider there are two obstacles in the environment.
If we want agents to pass between them, we need meters.

## Slide 12: OUR MODULATION
Given an agent A, the other agents around it are called NEIGHBORS.
We begin dividing the neighbors of A into three groups:
  Stuck neighbors:
    Their speed is less than 0.01 m/s
  Same-flow neighbors
    Their speed is greater than 0.01 m/s
    Their orientation differs from A’s at most 60º
  Opposite-flow neighbors
    Their speed is greater than 0.01 m/s
    Their orientation differs from A’s more than 60º

## Slide 13: OUR MODULATION: NARROW REGIONS
In the first place, we look for NARROW REGIONS.
We create the F-graph F=(VF , EF), where:
  Each node in VF correspond to a FIXED obstacle (walls, static obstacles and stuck neighbors)
  Two nodes in VF are connected by an edge if their distance is less than 2r + 2m.
If two nodes are connected, it is impossible for A to pass between the obstacles.

## Slide 14: OUR MODULATION: NARROW REGIONS
Example of F-graph:

## Slide 15: OUR MODULATION: NARROW REGIONS
We now define the set of narrow pairs:
A narrow pair is a pair of obstacles that let one, but not two, agents pass at once.
For each narrow pair , we define its narrow region as:
This is the set of points where A is blocking the narrow area between and .

## Slide 16: OUR MODULATION: NARROW REGIONS
We define the global narrow region as:
Each connected component of R is called a local narrow region.

## Slide 17: OUR MODULATION: NARROW REGIONS
Let Rmin the closest local narrow region that agent A is looking at.
  If an opposite-flow neighbor is in Rmin, A must stop until Rmin is empty.
  If an opposite-flow neighbor can reach Rmin before A, A must stop until Rmin is empty.
  In any other case, A can continue normally.
This way, the agents tend to wait each other when arriving to a narrow region.

## Slide 18: OUR MODULATION: OBSTRUCTIVE PLATOONS
After checking the narrow regions, we look for OBSTRUCTIVE PLATOONS.
We create the SA-graph SA = (VSA,ESA), where:
  VSA is formed by agent A and its same-flow neighbors
  Two nodes in VSA are connected by an edge if their distance is less than 2r + 2m
The PA-graph PA=(VPA,EPA) is the connected component of SA containing node A

## Slide 19: OUR MODULATION: OBSTRUCTIVE PLATOONS
Example of PA-graph:
A
n0
n1

## Slide 20: OUR MODULATION: OBSTRUCTIVE PLATOONS
We now create the FPA-graph FPA = (VFPA,EFPA), where:
  VFPA is the union of VF and VPA
  EFPA contains EF and EPA
  A node in VF and a node in VPA define an edge if their distance is less than 2r+2m

## Slide 21: OUR MODULATION: OBSTRUCTIVE PLATOONS
Example of FPA-graph:
A
n0
n1
w1
w0

## Slide 22: OUR MODULATION: OBSTRUCTIVE PLATOONS
We say that the platoon of A is blocking the space if we can find two nodes u, v in VF such that:
  u and v are in VFPA
  u and v are not path-connected in the F-graph
  u and v are path-connected in the FPA-graph
That is, the platoon is creating a blockage if it fills the space between two non-adjacent fixed obstacles.

## Slide 23: OUR MODULATION: OBSTRUCTIVE PLATOONS
In this example, the platoon of agent A is blocking the corridor.
A
n0
n1
w1
w0

## Slide 24: OUR MODULATION: OBSTRUCTIVE PLATOONS
What to do if A’s platoon is blocking the space?
  If A finds n platoon neighbors ahead, it multiplies its optimal speed by (3/4)n
  If A finds any platoon neighbor at its right, we create a virtual wall in front of A so the navigation behavior tries to avoid it going right.
This way, the agents tend to form a line until the blockage disappears.

## Slide 25: OUR MODULATION AVOIDS NEGATIVE EVENTS
Thanks to the modulation, the agents wait each other when reaching a door
Thanks to the modulation, the agents break the blockages and form lanes

## Slide 26: EXPERIMENTS

## Slide 27: Home scenario
To test this modulation, we designed a custom scenario simulating a building with:
  3 individual rooms
  A common area
  A corridor connecting them

## Slide 28: Home scenario
We ran 200 simulations of 120 seconds each one:
  In 100 of them, the agents used HL behavior only
  In 100 of them, the agents used HL behavior with our modulation
In each simulation, we counted:
  Total number of collisions
  Nº of agents that get stuck (deadlocks)

## Slide 29: Home scenario
The statistics of collisions and deadlocks improve when we apply our modulation.

## Slide 30: THANK YOU SO MUCH FOR YOUR TIME
Code for the modulation
and the experiments